## Slide 1
MOD·01
SAFETY MODULE
Electrical &
Board Safety
How to protect yourself — and the boards you're repairing — before you pick up a tool.
SHOCK
FIRE
ESD
CAPACITOR
PPE

## Slide 2
MOD·01
SAFETY · OVERVIEW
The Five Things That Can Hurt You (or Your Board)
Know these before you touch a live circuit — or a "dead" one.
Shock
Current through your body
100 mA
Fire
Shorted or overloaded parts
Class C
ESD
Static that kills silently
100 V
Charged Caps
Energy stored after power-off
Hours
Fumes
Solder flux and burnt parts
Ventilate

## Slide 3
MOD·01
SAFETY · SHOCK
What Is Electric Shock?
Current finds the fastest path to earth — even through you.
In Plain Terms
Current from a live point flows through your body the moment you become part of its path back to earth.
Real-World Picture
Like water finding the fastest way downhill — electricity finds the fastest way to earth, even through you.
Key Facts
It's current (mA), not voltage, that injures you. Dry skin resists current; sweat or a cut lowers that resistance fast.
230V mains = danger

## Slide 4
MOD·01
SAFETY · SHOCK
Why It's Dangerous
Current, not voltage, decides the outcome.
1
1 mA
Just a tingle
2
10 mA
Muscles lock — you can't let go
3
30 mA
Breathing becomes difficult
4
100+ mA
Can stop the heart — fatal
Household mains can push far more than this

## Slide 5
MOD·01
SAFETY · EXAMPLE
Real Example: A Shock Near-Miss
A "quick check" that nearly ended badly.
The Scenario
A technician probes a charger board still plugged in, keeping both hands on the case to steady it.
What Went Wrong
Both hands gave current a path straight across the chest — the one-hand rule was skipped for speed.
How to Prevent It
Isolate the supply first, or keep one hand behind your back if a live test is truly unavoidable.
Two hands on a live board is the danger

## Slide 6
MOD·01
SAFETY · SHOCK
Stay Safe on the Bench
A few habits keep every job routine.
HOW TO STAY SAFE
1
Isolate the supply before you start
2
Discharge capacitors first
3
Ground yourself and the bench
4
Keep one hand free during live tests
WARNING SIGNS
!
Board is warm or smells burnt
!
Exposed or frayed wiring
!
Meter still reads voltage on a 'dead' board
Confirm 0V before you touch anything

## Slide 7
MOD·01
SAFETY · SHOCK
Levels of Electrical Hazard
Not every job carries the same risk — know which you’re facing.
1
Low voltage (<50V)
USB, battery-powered boards — low risk, still respect polarity and shorts
2
Mains voltage (230V)
Chargers, power supplies — the everyday danger zone on the bench
3
Stored high energy
Charged capacitors and CRTs — dangerous even with the power unplugged
4
Industrial / 3-phase
Motor drives and factory equipment — always isolate and lock out first
Match your precautions to the hazard level

## Slide 8
MOD·01
SAFETY · BOARD SAFETY
What Is ESD?
Static you can't feel can still kill a chip.
In Plain Terms
Static builds up on your body and discharges the instant you touch a part — often with no shock you can even feel.
Real-World Picture
Like the hidden zap from a doorknob after walking on carpet — except this "zap" can leave a chip silently dead.
Key Facts
You feel a static spark at ~3,000V. Many ICs are destroyed by as little as 100V — thirty times less.
100V can destroy a chip

## Slide 9
MOD·01
SAFETY · BOARD SAFETY
Why It Damages Boards
The board doesn't spark, smoke, or complain — it just stops working.
1
Silent damage
No spark, no shock, no warning — the chip is just quietly dead
2
Cumulative harm
A part weakened by one shock can fail completely on the next
3
Built by walking
Ordinary movement across a floor can build thousands of volts
4
Worse in dry air
Low-humidity conditions make static build-up far worse
ESD damage stays invisible until the board fails

## Slide 10
MOD·01
SAFETY · EXAMPLE
Real Example: A Board Killed by Static
No spark. No smell. Just a board that never woke up again.
The Scenario
A technician unpacks a new replacement IC and fits it straight from the bag, no strap, no mat.
What Went Wrong
Static from ordinary movement discharged through the pins the instant the chip was handled.
How to Prevent It
Ground yourself before opening the bag, and place the part straight onto a grounded ESD mat.
The damage happened before the chip was even placed

## Slide 11
MOD·01
SAFETY · BOARD SAFETY
What Is a Charged Capacitor?
The board can be "off" and still be live inside.
In Plain Terms
Large capacitors store energy and can hold a charge for minutes — even hours — after the power is switched off.
Real-World Picture
Like a water tank that keeps draining long after the tap is closed — the charge has to go somewhere.
Key Facts
A shorted charged capacitor can spark, damage the board, and shock you — even on a fully unplugged unit.
Can stay charged for hours

## Slide 12
MOD·01
SAFETY · BOARD SAFETY
Protect the Board, Every Time
The same habits that protect you also protect what you’re fixing.
HOW TO DO IT RIGHT
1
Wear a grounded wrist strap
2
Work on a grounded ESD mat
3
Discharge caps with an insulated resistor
4
Confirm 0V before you touch a lead
WHAT GOES WRONG
!
Shorting capacitor legs with a bare screwdriver
!
Skipping the wait and diving straight in
!
Handling boards without grounding first
A resistor discharges safely — metal doesn’t

## Slide 13
MOD·01
SAFETY · PPE & PROCEDURE
Gear Up Before You Begin
Two minutes of setup beats an afternoon of downtime.
Wrist Strap
Grounded to the bench
Earth
ESD Mat
Grounded work surface
Grounded
Safety Glasses
For solder & caps
Always
Insulated Tools
Rated for live work
Rated
CAT Meter
Matched to the voltage
CAT II+

## Slide 14
MOD·01
SAFETY · PPE & PROCEDURE
Pre-Work Checklist
Every board, every time — no exceptions.
1
Visually inspect
Burnt tracks, bulging caps, exposed wires — before power
2
Isolate the supply
Unplug or switch off at the source, not just the load
3
Discharge capacitors
Bleed down stored charge, then confirm with a meter
4
Ground yourself
Wrist strap on, ESD mat connected, then begin
Skipping a step is how boards — and people — get hurt

## Slide 15
MOD·01
SAFETY · PPE & PROCEDURE
Spot the Hazard on a Real Board
Train your eyes before you ever pick up a meter.
1
Burnt or discoloured tracks
A sign of overcurrent or a short somewhere on that path
2
Bulging or vented capacitors
Stored energy may still be present — treat with care
3
Corroded or crusty pins
Leaked electrolyte or moisture damage, often spreading
4
Melted or cracked connectors
Overheating from a poor connection or an overloaded circuit
If it looks wrong, treat it as live until proven otherwise

## Slide 16
MOD·01
SAFETY · LIVE WORK & FIRE
When You Must Test Live
Sometimes the fault only shows up powered on.
1
One-hand rule
Keep your free hand off the chassis or any earthed surface
2
Match the CAT rating
A CAT I meter on mains wiring is a hazard, not a shortcut
3
Don't work alone
Someone nearby who can cut power and call for help
4
Dry hands, good light
Never test with wet hands or in a poorly lit area
Live testing is deliberate, never casual

## Slide 17
MOD·01
SAFETY · LIVE WORK & FIRE
Soldering & Thermal Safety
Heat, fumes, and molten metal — respect all three.
GOLDEN RULES
1
Iron runs at 300–400°C — hot enough to burn instantly
2
Always return it to its stand, never the bench
3
Work with ventilation — flux fumes irritate the lungs
IF YOU GET BURNED
!
Cool under running water for at least 10 minutes
!
Never apply ice, butter, or ointments
!
Cover loosely and seek care if it’s serious
Keep your face back — solder can flick

## Slide 18
MOD·01
SAFETY · LIVE WORK & FIRE
Fire Sources on a Repair Bench
Most bench fires trace back to one of these four.
1
Shorted battery pack
A punctured or bridged cell can ignite in seconds
2
Overloaded bench supply
No current limit set, feeding a fault more power than it can handle
3
Faulty charger left running
Unattended and already showing signs of overheating
4
Damaged insulation
Bare wire resting against a live point or metal chassis
Most bench fires are preventable, not accidental

## Slide 19
MOD·01
SAFETY · LIVE WORK & FIRE
If a Board Catches Fire
Water and electricity are a dangerous mix — never combine them.
DO THIS
1
Cut power at the source if it’s safe to reach
2
Use a Class C extinguisher, aimed at the base
3
Alert others in the workshop immediately
NEVER DO THIS
!
Throw water on an electrical fire
!
Use a Class A extinguisher on live equipment
!
Fight a fire that’s already spreading — evacuate
Know your nearest extinguisher before you need it

## Slide 20
MOD·01
SAFETY · EXAMPLE
Real Example: A Close Call With Fire
An unattended charger, and a smoke smell that ended it early.
The Scenario
A faulty charger is left plugged in and running overnight on a test bench with no one nearby.
What Went Wrong
An overloaded, unattended charger began overheating with nobody there to notice in time.
How to Prevent It
Never leave a suspect device powered and unattended — test it, then switch it off.
Unattended power is how small faults become fires

## Slide 21
MOD·01
SAFETY · EMERGENCY
If Someone Is Being Shocked
Do not touch them directly — you’ll become a second casualty.
1
Cut the power
Switch off or unplug the source immediately, if reachable
2
Separate with an insulator
A dry wooden or plastic object — never your bare hands
3
Call for emergency help
Get trained medical assistance on the way
4
Check breathing
If trained in CPR and breathing has stopped, begin CPR
Seconds matter — act, don’t freeze

## Slide 22
MOD·01
SAFETY · PRACTICAL
Practical Exercise: Make a Board Safe
Working in pairs, take an unpowered SMPS board and complete this list.
✓
Visually inspect the board and note any damage
✓
Confirm the board is unplugged and switched off
✓
Locate the main filter capacitor(s) on the board
✓
Discharge the capacitor with an insulated resistor
✓
Confirm 0V with a multimeter before touching a lead
✓
Put on your wrist strap, connect it, then proceed
Have your instructor sign off before you continue

## Slide 23
MOD·01
SAFETY · REPAIR EXERCISE
Repair Exercise: What Went Wrong?
A technician was rushed into hospital after this repair. Find the missed step.
The Scenario
A recently-repaired power supply is handed back for a "quick recheck" — still warm from the last test.
What Went Wrong
It was opened and probed immediately, with no wait, no discharge, and no meter check first.
How to Prevent It
Every board gets the same pre-work checklist — "quick recheck" is not an exception.
There are no shortcuts on a "quick" job

## Slide 24
MOD·01
SAFETY · QUIZ
Quick Check
Talk through these before moving on to Module 2.
1
Question 1
Why is current, not voltage, the number that decides how dangerous a shock is?
2
Question 2
A board has been unplugged for five minutes — is it definitely safe to touch?
3
Question 3
Why can a component be damaged by static you never even felt?
4
Question 4
What is the very first thing you should NOT do for someone being shocked?
Discuss as a group before checking the answer key

## Slide 25
MOD·01
SAFETY · QUICK REFERENCE
Quick Safety Reference
One line per hazard — what to check, and what tells you it’s safe.
HAZARD
CHECK WITH
SAFE STATE
DANGER SIGN
Shock
Multimeter
0V confirmed
Any voltage reading
Charged Cap
Insulated resistor
Discharged, 0V
Warm or bulging body
ESD
Wrist strap + mat
Grounded before touch
No strap, dry air
Fire
Class C extinguisher
Power cut, area clear
Smoke or burning smell
Burn
Iron on its stand
Tip stored, cooled
Iron left on the bench

## Slide 26
MOD·01
MODULE WRAP-UP
You Can Now…
By the end of this module, every recruit should be able to:
✓
Explain why current, not voltage, is what injures you
✓
Identify and safely discharge a charged capacitor
✓
Protect a board from ESD with a strap and a mat
✓
Follow the pre-work checklist before every repair
✓
Respond correctly to a shock, burn, or bench fire
!
GOLDEN RULE
Power off and discharge capacitors — and ground yourself — before you probe anything.