## Slide 1
MOD·02
WORKSHOP MODULE
Workshop
Skills
The bench, the tools, and the techniques every repair starts with.
HAND TOOLS
SOLDER
DESOLDER
METER
INSPECT

## Slide 2
MOD·02
WORKSHOP · OVERVIEW
The Five Skills Every Bench Runs On
Master these before you touch your first real repair.
Hand Tools
Drivers, cutters, tweezers
Daily use
Soldering
Joining components to a board
300–400°C
Desoldering
Removing parts cleanly
Wick / pump
Multimeter
Your first diagnostic tool
V · Ω · A
Inspection
Reading a board before you touch it
Magnify

## Slide 3
MOD·02
WORKSHOP · BENCH
What Is a Repair Bench?
Your results are only as good as the space you build them in.
In Plain Terms
A dedicated, organised, well-lit surface where every tool has a fixed place and every board has room to breathe.
Real-World Picture
Like a surgeon's tray — instruments laid out, nothing loose, nothing in the way of the next move.
Key Facts
Grounded ESD mat, bright lighting, and a fire extinguisher within reach — non-negotiable basics.
ESD mat + good light = ready

## Slide 4
MOD·02
WORKSHOP · BENCH
Essential Hand Tools
Five tools that live on every bench, every day.
1
Screwdriver set
Phillips, flathead, and precision bits for tiny casing screws
2
Cutters & pliers
Flush cutters for leads, long-nose pliers for bending and holding
3
Tweezers
Fine-tipped, for placing and lifting small SMD parts
4
Spudgers & prying tools
Plastic, non-conductive — for opening cases without scratches
Right tool, right job — every time

## Slide 5
MOD·02
WORKSHOP · BENCH
Choosing Between Hand Tools
Similar tools, different jobs — pick with intent.
1
Screwdriver vs nut driver
Nut drivers grip hex fasteners without camming out like a screwdriver can
2
Cutters vs long-nose pliers
Cutters trim; long-nose pliers bend, hold, and reach into tight spots
3
Metal vs plastic spudger
Plastic protects delicate plastics and ribbon cables; metal is for tougher clips
4
Fine vs standard tweezers
Fine tips for SMD placement; standard tips for general handling
The wrong tool damages the part it’s meant to help

## Slide 6
MOD·02
WORKSHOP · BENCH
Setting Up Your Station
Two minutes of setup saves an hour of searching.
HOW TO SET UP
1
Clear the surface — one board at a time
2
ESD mat down and grounded first
3
Tools within arm’s reach, in fixed spots
4
Good overhead light plus a task lamp
COMMON MISTAKES
!
Working on a cluttered or shared surface
!
No ESD protection on the bench
!
Cables and tools crossing the work area
A tidy bench is a safe, fast bench

## Slide 7
MOD·02
WORKSHOP · SOLDERING
What Is Soldering?
Melting metal to make a permanent electrical joint.
In Plain Terms
Heat and solder join a component lead to a copper pad, creating both a mechanical bond and an electrical path.
Real-World Picture
Like welding in miniature — two metal surfaces fused together by a third, molten one.
Key Facts
A good joint is shiny and cone-shaped. A dull, cracked, or blobby joint is a fault waiting to happen.
Iron tip: 300–400°C

## Slide 8
MOD·02
WORKSHOP · SOLDERING
Iron Wattage & Tip Shapes
The right shape and power for the joint in front of you.
1
Conical tip
General-purpose — fine point for precise, everyday joints
2
Chisel tip
Wider, flat edge — better heat transfer for larger pads and wires
3
Micro / needle tip
Fine SMD work where neighbouring pads sit close together
4
15–40W vs 60W+
Lower wattage for delicate boards; higher for ground planes and thick wire
Match the tip to the joint, not the other way round

## Slide 9
MOD·02
WORKSHOP · SOLDERING
Choosing the Right Tip & Temperature
Too cold gives a bad joint. Too hot damages the board.
In Plain Terms
Temperature and tip shape both need to match the joint — too little heat won’t flow solder, too much lifts pads.
Real-World Picture
Like cooking on a stove — the right heat cooks evenly; too high just burns the outside.
Key Facts
Most work sits around 300–350°C. Ground planes and thick pads may need a little more.
350°C covers most everyday joints

## Slide 10
MOD·02
WORKSHOP · SOLDERING
The Soldering Process
Four steps, done the same way, every single joint.
1
Heat the joint
Touch the iron to both the pad and the lead together, not the solder
2
Feed the solder
Melt solder onto the heated joint — not onto the iron tip
3
Remove heat, then solder
Pull the iron away first, then the solder, and let it set
4
Inspect the result
Shiny, cone-shaped, no bridges to neighbouring pads
Heat the joint — not the solder

## Slide 11
MOD·02
WORKSHOP · SOLDERING
Get a Good Joint, Every Time
Your eyes catch most faults before a meter ever does.
GOOD JOINT SIGNS
1
Smooth, shiny, cone-shaped finish
2
Solder flows fully onto pad and lead
3
No excess solder or stray bridges
BAD JOINT SIGNS
!
Dull, grainy, or cracked surface — a cold joint
!
Solder balled up, not wetted to the pad
!
Bridges connecting two separate pads
A bright light and a loupe catch what eyes alone miss

## Slide 12
MOD·02
WORKSHOP · EXAMPLE
Real Example: Soldering a Cracked Joint
A phone that only charged when the cable was wiggled.
The Scenario
A charging port works intermittently — jiggling the cable sometimes brings it back to life.
What You Do
Inspect the port’s solder joints under magnification and reflow any that look dull or cracked.
What It Tells You
A cracked joint was making and breaking contact — reflowing it restores a solid connection.
Intermittent faults often trace back to one bad joint

## Slide 13
MOD·02
WORKSHOP · DESOLDERING
What Is Desoldering?
Removing a part cleanly, without damaging the board.
In Plain Terms
Re-melting existing solder so a component can be lifted free, leaving the pad and track intact.
Real-World Picture
Like carefully un-gluing something without tearing the paper underneath.
Key Facts
Rushed desoldering is the single biggest cause of lifted pads and ruined boards — patience matters more than speed.
Slow and controlled beats fast and forced

## Slide 14
MOD·02
WORKSHOP · DESOLDERING
Desoldering Tools & Methods
Pick the tool that matches the joint.
1
Solder wick
Copper braid that soaks up melted solder — best for flat pads
2
Solder sucker (pump)
Spring-loaded vacuum that pulls molten solder from a hole
3
Hot air rework station
Even heat for multi-leg parts like ICs — no direct contact
4
Iron + wick combo
The everyday go-to for most through-hole components
Match the tool to the joint, not habit

## Slide 15
MOD·02
WORKSHOP · EXAMPLE
Real Example: Desoldering an IC Without Lifting Pads
Sixteen legs, one chance to get it right.
The Scenario
A faulty 16-pin IC needs replacing on a densely-packed board with no room for a heavy hand.
What You Do
Apply even hot air across all legs at once, then lift the chip once every joint has released.
What It Tells You
Even heating avoids the twisting force that tears a pad off a single-point iron approach.
Heat evenly, lift once, never pry against a pad

## Slide 16
MOD·02
WORKSHOP · MATERIALS
Types of Solder & Flux
The metal and the chemistry behind every joint.
1
Leaded solder (60/40)
Lower melting point, easier to work with — common in repair shops
2
Lead-free solder
Higher melting point, required for many new consumer products
3
Flux-core wire
Flux built into the solder itself for everyday joints
4
Liquid / paste flux
Applied separately for stubborn joints and SMD rework
Flux is what makes solder flow, not just melt

## Slide 17
MOD·02
WORKSHOP · MATERIALS
Reading Tool & Wire Markings
Small print, important information.
1
Solder diameter & alloy
Printed on the spool — e.g. 0.8mm, Sn60Pb40
2
Wire gauge (AWG)
Smaller number means thicker wire and higher current capacity
3
Screwdriver tip size
Printed on the shaft — PH0, PH1, flat 3mm, and so on
4
Iron wattage
Printed on the handle or base — matches the tip guidance from earlier
Five seconds reading a label saves a mismatched joint

## Slide 18
MOD·02
WORKSHOP · TEST EQUIPMENT
The Multimeter — Your First Tool
One instrument, and you can diagnose most faults.
In Plain Terms
A single meter that measures voltage, resistance, continuity, and current — the first thing you reach for.
Real-World Picture
Like a doctor's stethoscope — quick checks that tell you where to look closer.
Key Facts
Always start on the highest safe range, and use a CAT-rated meter matched to what you’re testing.
One meter, most answers

## Slide 19
MOD·02
WORKSHOP · TEST EQUIPMENT
Multimeter Settings You’ll Use
The four modes that cover most bench work.
1
Voltage (V)
Confirms power is present — and how much of it
2
Resistance (Ω)
Checks a component’s value, out of circuit
3
Continuity / diode mode
Beeps on a closed path — fast fault-finding
4
Current (A)
Measured in series — rarely needed, easy to get wrong
When in doubt, start on the highest range

## Slide 20
MOD·02
WORKSHOP · TEST EQUIPMENT
Reading the Display Right
The meter is only as good as the read.
HOW TO READ IT
1
Match the probe colours: red = positive, black = common
2
Wait for the reading to settle before recording it
3
Zero the leads on resistance mode first
COMMON MISTAKES
!
Leaving the meter on the wrong function
!
Probing with the leads in the wrong sockets
!
Trusting a reading that’s still jumping around
A steady reading is a trustworthy reading

## Slide 21
MOD·02
WORKSHOP · INSPECTION
Inspecting a Board
Look before you touch — most clues are visible.
1
Visual scan
Burn marks, bulging caps, cracked solder, corrosion
2
Magnification
A loupe or microscope reveals hairline cracks the eye misses
3
Cleaning first
Isopropyl alcohol removes flux and grime hiding faults
4
Document what you find
Photos and notes before you start — for reference and proof
The fault is often visible before the meter confirms it

## Slide 22
MOD·02
WORKSHOP · TOOL CARE
Cleaning & Maintaining Your Tools
A well-kept tool works better and lasts longer.
1
Tin the tip before storing
A thin layer of solder stops the tip oxidising between jobs
2
Clean on a damp sponge or brass
Wipe off old solder before every new joint
3
Wipe down the ESD mat
Flux residue and grime break down its grounding over time
4
Check calibration periodically
A meter or ESR tester that’s drifted gives false confidence
Five minutes of care saves an hour of chasing bad readings

## Slide 23
MOD·02
WORKSHOP · TOOL CARE
Common Bench Tool Failures
Know when to clean it, and when to retire it.
STILL SERVICEABLE
1
Tip is oxidised but responds to cleaning and re-tinning
2
Cutters are slightly dull but still cut cleanly
3
Wick is used but still absorbs solder well
TIME TO REPLACE
!
Tip is pitted, worn flat, or won’t hold solder
!
Cutters leave a ragged, torn edge on leads
!
Meter leads are cracked or reading inconsistently
A worn tool causes the faults you’re trying to fix

## Slide 24
MOD·02
WORKSHOP · PRACTICAL
Practical Exercise: Solder Ten Clean Joints
Work through this list on a practice board before moving to a real repair.
✓
Set up your station — ESD mat, wrist strap, iron on its stand
✓
Set the iron to the correct temperature for the joint
✓
Solder ten through-hole joints on a practice board
✓
Inspect each joint under magnification
✓
Reflow any joint that looks dull, cracked, or blobby
✓
Have your instructor check the finished board
Aim for ten clean joints in a row, not just one

## Slide 25
MOD·02
WORKSHOP · REPAIR EXERCISE
Repair Exercise: Fix the Bad Joint
A practice board comes back with five deliberately bad joints.
The Scenario
Five joints on the board are cold, bridged, or starved of solder — on purpose, for practice.
What You Do
Identify each fault by eye first, then confirm with a loupe before touching the iron.
What It Tells You
Reflowing without diagnosing first often just hides a fault instead of fixing it.
Diagnose the joint before you reach for the iron

## Slide 26
MOD·02
WORKSHOP · QUIZ
Quick Check
Talk through these before moving on to Module 3.
1
Question 1
What does a shiny, cone-shaped joint tell you that a dull one doesn’t?
2
Question 2
Why is rushing a desoldering job the most common cause of lifted pads?
3
Question 3
When would you reach for hot air instead of an iron and wick?
4
Question 4
What are two signs a soldering iron tip needs replacing, not just cleaning?
Discuss as a group before checking the answer key

## Slide 27
MOD·02
WORKSHOP · QUICK REFERENCE
Quick Tool Reference
One line per tool — what it’s for, and what to watch for.
TOOL
USE FOR
TYPICAL SETTING
WATCH FOR
Soldering iron
Joining leads to pads
300–400°C
Cold, dull joints
Solder wick
Lifting solder off a pad
Fresh braid
Lifted or torn pads
Multimeter
Voltage, Ω, continuity
CAT II+
Wrong function selected
Tweezers
Placing small SMD parts
Fine tip
Static damage without a strap
Loupe / microscope
Close inspection
10–20x
Missed hairline cracks

## Slide 28
MOD·02
MODULE WRAP-UP
You Can Now…
By the end of this module, every recruit should be able to:
✓
Set up an organised, ESD-safe repair bench
✓
Solder a clean, reliable joint from scratch
✓
Desolder a part without damaging the board
✓
Use a multimeter’s core settings with confidence
✓
Visually inspect a board before powering it on
!
GOLDEN RULE
A tidy, grounded bench prevents more faults than any single tool ever fixes.