## Slide 1
MOD·04
REWORK MODULE
Soldering &
PCB Rework
Removing, fixing, and reinstalling components without damaging the board.
SOLDER
DESOLDER
REWORK
BGA
INSPECT

## Slide 2
MOD·04
REWORK · OVERVIEW
The Five Skills of PCB Rework
From a clean joint to a fully reworked board.
Soldering
Through-hole and SMD joints
300–400°C
Desoldering
Removing parts cleanly
No lifted pads
Component Swap
Right method per part type
IC vs board
BGA Rework
Chips with hidden solder balls
Hot air
Inspection
Verifying the repair holds
Clean + test

## Slide 3
MOD·04
REWORK · WARM-UP
Before We Start…
A quick show of hands before we open a single board.
Have you ever opened up a TV, radio, or mobile phone to try and fix it?
Think about what you found inside — and what you would do differently now.

## Slide 4
MOD·04
REWORK · SOLDERING
Why Soldering Matters Here
Every rework job starts and ends with a joint.
In Plain Terms
Rework soldering isn’t factory assembly — it’s precise, one-off work on a board that’s already built and populated.
Real-World Picture
Like re-stitching one seam on a finished garment, without disturbing anything around it.
Key Facts
A rework joint has less margin for error — neighbouring parts, heat-sensitive plastics, and tiny pads are all close by.
Precision matters more than speed

## Slide 5
MOD·04
REWORK · SOLDERING
Iron & Station Tools
The core equipment behind every rework bench.
1
Soldering iron
Fine-tip, temperature-controlled — for through-hole and simple SMD work
2
Hot air rework station
Even, contactless heat for multi-leg SMD parts and BGAs
3
Iron stand & sponge
Keeps the tip safe, clean, and ready between joints
4
Fume extractor
Pulls flux fumes away from your face during long rework sessions
A fume extractor is not optional for daily rework

## Slide 6
MOD·04
REWORK · SOLDERING
Solder & Flux Materials
The right metal and chemistry for the job.
1
Leaded solder (60/40)
Lower melting point — easier control for delicate rework
2
Lead-free solder
Higher melting point, required to match many original assemblies
3
Flux-core wire
Built-in flux for everyday through-hole joints
4
Solder paste
Pre-measured solder and flux, used with hot air for SMD rework
Fresh flux is the difference between a joint and a blob

## Slide 7
MOD·04
REWORK · SOLDERING
Through-Hole Soldering: How To
The same four steps, every single joint.
1
Insert the lead
Seat the component fully against the board before heating anything
2
Heat pad and lead together
Touch the iron to both surfaces, not just the wire
3
Feed the solder
Melt it onto the heated joint, not onto the iron tip itself
4
Trim and inspect
Cut excess lead, then check for a shiny, cone-shaped result
Heat the joint — the solder follows the heat

## Slide 8
MOD·04
REWORK · SOLDERING
SMD Soldering Basics
Smaller pads, smaller margin for error.
In Plain Terms
Surface-mount parts sit directly on the pad with no hole to anchor them — precision and a steady hand matter more.
Real-World Picture
Like placing a coin on a table and gluing it down, instead of pushing it through a slot.
Key Facts
A fine conical tip, a magnifier, and a steady hand handle most SMD joints without needing hot air.
Fine tip + magnification = confident SMD work

## Slide 9
MOD·04
REWORK · SOLDERING
Common Solder Defects
Spot these before you move on to the next joint.
GOOD JOINT SIGNS
1
Smooth, shiny, cone-shaped finish
2
Solder wets fully onto both pad and lead
3
No bridges to neighbouring pads
DEFECT SIGNS
!
Cold joint — dull, grainy, or cracked
!
Bridging — solder connecting two separate pads
!
Tombstoning — one end lifts as the other cools
Most defects are visible before they ever fail a test

## Slide 10
MOD·04
REWORK · EXAMPLE
Real Example: TV Repair
A TV that wouldn’t turn on, traced to one bad joint.
The Scenario
A television is completely dead. No lights, no sound, nothing on the screen at all.
What You Do
Inspect the power board under magnification and spot a cracked joint on the main fuse.
What It Tells You
A single cold joint on a fuse leg had broken the entire power path to the rest of the set.
One bad joint can look exactly like a dead board

## Slide 11
MOD·04
REWORK · DESOLDERING
Desoldering for Rework
Getting a part off without taking the pad with it.
1
Solder wick
Copper braid that lifts solder from flat, accessible pads
2
Solder sucker (pump)
Vacuum-pulls molten solder out of a through-hole
3
Hot air station
Even heat across every leg of an SMD part at once
4
Iron + wick combo
The everyday choice for most through-hole rework
Rushed desoldering is how pads get lifted

## Slide 12
MOD·04
REWORK · PCB REWORK
What Is PCB Rework?
Repairing the board itself, not just the parts on it.
In Plain Terms
Rework is the process of removing, replacing, or repairing a component or the board area around it.
Real-World Picture
Like replacing a single tile on a roof instead of re-roofing the whole house.
Key Facts
Good rework leaves no trace — same footprint, same pad condition, same board integrity as before the fault.
The goal: no trace it was ever repaired

## Slide 13
MOD·04
REWORK · PCB REWORK
Rework Tools by Name
Beyond the iron — the equipment dedicated rework needs.
1
Hot air rework station
Adjustable temperature and airflow for SMD and BGA removal
2
Preheater
Warms the whole board evenly, reducing thermal shock and warping
3
BGA rework station
Combines preheat, top heat, and precise placement for BGA chips
4
Microscope / loupe
Close inspection of fine-pitch parts and hairline defects
The right station turns a risky job into a routine one

## Slide 14
MOD·04
REWORK · PCB REWORK
Component Removal: How To
Four steps that protect the pad underneath.
1
Heat evenly
Warm every leg or side together — never force one point alone
2
Lift gently
Let the part come free on its own once every joint has released
3
Clean the pad
Remove leftover solder before anything goes back down
4
Inspect for damage
Check the pad and surrounding tracks before reinstalling
Never pry against a pad that hasn’t fully released

## Slide 15
MOD·04
REWORK · PCB REWORK
Removal Method by Component Type
Match the method to the part — one approach doesn’t fit all.
COMPONENT
METHOD
TOOL
RISK
Through-hole R/C
Heat both sides, pull
Iron + wick
Low, with patience
SMD 2-pin part
Heat both pads together
Iron or hot air
Tombstoning if uneven
SMD IC (multi-leg)
Even heat, all legs at once
Hot air station
Lifted pads if rushed
BGA chip
Preheat, then top heat
BGA rework station
Board warping if uneven

## Slide 16
MOD·04
REWORK · PCB REWORK
Fixing & Reinstalling a Component
Getting the replacement part back on cleanly.
1
Prep the pad
Clean, flat, and pre-tinned before the new part goes anywhere near it
2
Align the part
Match orientation and footprint exactly before any heat is applied
3
Tack one pin first
Secure one point, check alignment, then solder the rest
4
Solder the remaining pins
Work steadily around the part, checking each joint as you go
One tacked pin lets you fix alignment before it’s permanent

## Slide 17
MOD·04
REWORK · DECISION
IC-Only vs Whole-PCB Replacement
Not every fault means replacing the whole board.
REPLACE JUST THE IC
1
Fault is clearly localised to one component
2
Surrounding tracks and pads are undamaged
3
The part is available and reasonably reworkable
REPLACE THE WHOLE BOARD
!
Multiple tracks or layers are damaged
!
The pad or footprint is beyond repair
!
Rework cost approaches the price of a new board
Repair the smallest thing that fixes the fault

## Slide 18
MOD·04
REWORK · DECISION
Decision Matrix
A quick reference for the call you’ll make on the bench.
SYMPTOM
LIKELY CAUSE
FIX
WHY
One function fails
Single IC or part faulty
IC-only swap
Fault is localised
Board resets randomly
Weak capacitor or supply IC
IC-only swap
Still a single fault
Burn marks, multiple tracks
Cascading overcurrent damage
Whole-board swap
Repair cost exceeds part
Cracked or delaminated PCB
Physical / structural damage
Whole-board swap
Board integrity is gone

## Slide 19
MOD·04
REWORK · BGA
BGA Rework
The trickiest chip on the board — because you can’t see its joints.
In Plain Terms
A BGA chip connects to the board through a hidden grid of solder balls underneath it, not visible legs.
Real-World Picture
Like a plug with hundreds of tiny contacts hidden under its base — you can’t inspect a single one directly.
Key Facts
Removal and reinstallation need a hot air or BGA station, a stencil, and fresh solder balls — reballing, not just reheating.
You trust the process — you can’t see the joints

## Slide 20
MOD·04
REWORK · TRACK & PAD REPAIR
Track & Pad Repair
When the damage is the board itself, not the part.
1
Bridge a cut track
A fine jumper wire restores the broken connection
2
Rebuild a lifted pad
A small wire tacked to the nearest good point re-forms the pad
3
Patch with copper tape
Extends a damaged trace across a larger gap
4
Seal with lacquer
Protects the repaired area from moisture and future corrosion
A track repair is only as good as its mechanical strength

## Slide 21
MOD·04
REWORK · CLEANING & INSPECTION
Cleaning & Inspection After Rework
The job isn’t done until it’s verified.
1
Clean with isopropyl alcohol
Removes flux residue that can hide problems or attract moisture
2
Magnify every joint
A loupe or microscope catches what your eyes alone will miss
3
Continuity check
Confirm no bridges and no broken paths before power is applied
4
Power-on test
Verify the repaired function actually works, not just looks right
A clean board is easier to diagnose next time, too

## Slide 22
MOD·04
REWORK · SAFETY
Rework Safety
The same discipline from Module 1, applied to hot air and bare ICs.
HOW TO STAY SAFE
1
Run the fume extractor during every hot air job
2
Let hot air nozzles and boards cool before handling
3
Ground yourself before handling a bare, unpackaged IC
WARNING SIGNS
!
Burn marks appearing on nearby plastic parts
!
Board flexing or warping under heat
!
A component you’re not actively working on feels hot
Hot air is invisible heat — treat it with the same respect as an iron

## Slide 23
MOD·04
REWORK · EXAMPLE
Real Example: Mobile Charging IC
A phone that charged only if you held the cable just right.
The Scenario
A phone won’t charge reliably — wiggling the cable sometimes gets it going, sometimes not.
What You Do
Remove the charging IC with hot air, clean the pads, and reinstall a new one with a stencil.
What It Tells You
A cracked charging IC joint was intermittently breaking contact — a clean rework restored it.
Intermittent faults often live at exactly one joint

## Slide 24
MOD·04
REWORK · PRACTICAL
Practical Exercise: Rework a Test Board
Work through this list on a practice board before a real repair.
✓
Desolder a through-hole component without lifting the pad
✓
Desolder an SMD part using hot air, evenly across all legs
✓
Clean both pads before reinstalling anything
✓
Solder a replacement part, checking alignment before final joints
✓
Clean the area and inspect every joint under magnification
✓
Power on and confirm the function actually works
Aim for a repair that leaves no trace it happened

## Slide 25
MOD·04
REWORK · REPAIR EXERCISE
Repair Exercise: Diagnose the Mistake
A reworked board came back with the same fault.
The Scenario
An IC was replaced, but the board shows the exact same symptom it had before the repair.
What Went Wrong
The pad was damaged during removal and never inspected before the new part went on.
How to Prevent It
Always inspect the pad after removal, before reinstalling — a damaged pad needs repair first.
A repeat fault often means a step was skipped, not a bad part

## Slide 26
MOD·04
REWORK · QUICK REFERENCE
Quick Reference: Rework Temperatures
One line per task — tool, typical temperature, and the catch.
TASK
TOOL
TYPICAL TEMP
NOTES
Through-hole solder
Soldering iron
300–350°C
Higher for ground planes
SMD hot air removal
Hot air station
320–370°C
Even airflow, no direct point
BGA reflow
BGA / hot air station
220–245°C peak
Follow the solder profile
Desoldering wick
Iron + wick
300–350°C
Fresh braid absorbs better

## Slide 27
MOD·04
REWORK · QUIZ
Quick Check
Talk through these before moving on to Module 5.
1
Question 1
Why does a rework joint have less margin for error than a factory joint?
2
Question 2
What is the biggest risk of forcing a part off before every joint has released?
3
Question 3
Give one sign that a fault needs a whole-board swap, not just an IC swap.
4
Question 4
Why can’t you visually inspect a BGA chip’s solder joints directly?
Discuss as a group before checking the answer key

## Slide 28
MOD·04
MODULE WRAP-UP
You Can Now…
By the end of this module, every recruit should be able to:
✓
Solder a clean through-hole or SMD joint under rework conditions
✓
Remove a component without lifting a pad or damaging a track
✓
Decide between an IC-only swap and a whole-board replacement
✓
Rework a BGA chip using preheat, hot air, and reballing
✓
Clean, inspect, and verify a repair before calling it done
!
GOLDEN RULE
Good rework leaves no trace it ever happened — same footprint, same board, working part.