## Slide 1
MOD·05
CIRCUIT MODULE
Circuit
Building
From a schematic on paper to a working circuit on the bench.
SCHEMATIC
BREADBOARD
BUILD
TEST
DOCUMENT

## Slide 2
MOD·05
CIRCUIT · OVERVIEW
The Five Steps From Paper to Bench
Every project you build follows the same five stages.
Read It
Understand the schematic first
Symbols
Breadboard It
Prototype before anything permanent
No solder
Build It
Power, input, processing, output
4 blocks
Test It
Verify before and after power-on
Trace it
Document It
Record what you built and found
BOM + notes

## Slide 3
MOD·05
CIRCUIT · WARM-UP
Before We Start…
A quick check before we look at a single schematic.
Have you ever looked at a circuit diagram and had no idea where to even start?
Hold that thought — by the end of this module, any schematic will have a clear starting point.

## Slide 4
MOD·05
CIRCUIT · SCHEMATICS
What Is a Schematic?
A map of connections, not a picture of the parts.
In Plain Terms
A schematic shows how components connect to each other using symbols and lines — not what they physically look like.
Real-World Picture
Like a subway map — it shows connections and stops clearly, without drawing every street in between.
Key Facts
Signal generally flows left to right, power rails run top and bottom, and ground ties everything to a common reference.
Connections matter, not physical layout

## Slide 5
MOD·05
CIRCUIT · SCHEMATICS
Classifying Circuit Types
Know what kind of circuit you’re reading before you trace it.
1
Series vs parallel
Series shares one path; parallel splits current across multiple paths
2
Analog vs digital
Analog varies smoothly; digital switches between two clear states
3
AC vs DC
AC reverses direction periodically; DC flows one way, steadily
4
Simple vs complex
Complex circuits are just simple blocks connected together
Every complex circuit breaks down into simple ones

## Slide 6
MOD·05
CIRCUIT · SCHEMATICS
Common Schematic Symbols
A handful of symbols cover most of what you’ll read.
1
Resistor, capacitor, diode
The basic passive and semiconductor symbols from Module 4’s components
2
Ground symbol
The common reference point every voltage is measured against
3
Power rail labels
e.g. +5V, VCC, GND — named nets instead of drawn wires
4
IC block
A labelled rectangle with numbered pins — details live in its datasheet
A symbol you don’t recognise is one datasheet lookup away

## Slide 7
MOD·05
CIRCUIT · SCHEMATICS
Reading Signal Flow
Follow the path, not just the parts.
1
Start at the power source
Find where energy enters the circuit first
2
Follow left to right
Most schematics flow input to output in reading order
3
Watch for feedback loops
A line looping backward usually means feedback or control
4
Find the ground return
Every path eventually needs a way back to common
If you can trace the path, you can trace the fault

## Slide 8
MOD·05
CIRCUIT · EXAMPLE
Real Example: Tracing a Simple LED Circuit
Three symbols, one clear story.
The Scenario
A schematic shows a battery, a resistor, and an LED, all drawn in a single loop.
What You Do
Trace from the battery’s positive terminal, through the resistor, through the LED, back to negative.
What It Tells You
The resistor limits current before it ever reaches the LED — exactly why it’s placed there.
Tracing the path explains the purpose of every part

## Slide 9
MOD·05
CIRCUIT · BREADBOARDING
What Is a Breadboard?
A way to build and change a circuit without soldering a single joint.
In Plain Terms
A breadboard holds components and connects them through internal metal strips — no soldering needed to test an idea.
Real-World Picture
Like building with reusable blocks instead of gluing every piece down permanently.
Key Facts
It’s for prototyping only — never a permanent build, since connections can loosen with vibration or time.
Prototype first, solder later

## Slide 10
MOD·05
CIRCUIT · BREADBOARDING
How the Rows Connect
Knowing the hidden wiring saves you from confusing shorts.
1
Power rails (top & bottom)
Long strips running the full length, for +V and ground
2
Terminal strips (middle)
Short columns of five holes, all connected vertically
3
The centre gap
Separates the two halves — ICs usually straddle it
4
No connection across the gap
Assuming a connection there is a common wiring mistake
Five holes in a column are already connected — don’t double up

## Slide 11
MOD·05
CIRCUIT · BREADBOARDING
Breadboarding Do’s and Don’ts
Small habits that save a lot of confused troubleshooting.
DO THIS
1
Keep power and ground rails tidy and clearly routed
2
Trim leads so they seat firmly in the holes
3
Build and test one section before adding the next
DON’T DO THIS
!
Assume the centre gap is electrically connected
!
Leave loose, half-inserted leads
!
Build the entire circuit before testing any of it
A tidy breadboard is a debuggable breadboard

## Slide 12
MOD·05
CIRCUIT · BUILDING
The Four Building Blocks of Any Circuit
Every circuit, simple or complex, breaks down into these.
1
Power source
Battery, adapter, or bench supply — where the energy comes from
2
Input
Switches, sensors, or signals — where information enters
3
Processing
Transistors, ICs, or logic — where decisions are made
4
Output
LEDs, motors, or speakers — where the result appears
Complex circuits are just these four blocks, repeated

## Slide 13
MOD·05
CIRCUIT · BUILDING
Circuit Specifications That Matter
Numbers that decide whether a build survives first power-on.
Voltage rating
Every part has a maximum it can handle before it fails
Current rating
How much current a part or wire can safely carry continuously
Power dissipation
Heat a component must shed — exceeding it leads to failure
Check ratings before power, not after smoke

## Slide 14
MOD·05
CIRCUIT · BUILDING
From Schematic to Breadboard
Turning the diagram into something physical, one step at a time.
1
Identify the four blocks
Mark power, input, processing, and output on the schematic first
2
Place power rails first
Wire +V and ground before placing a single component
3
Place components by block
Work through power, then input, then processing, then output
4
Wire the connections last
Follow the schematic’s lines exactly, one net at a time
Power and ground first, always

## Slide 15
MOD·05
CIRCUIT · EXAMPLE
Real Example: Building an LED Torch
The simplest project that still teaches every step.
The Scenario
A battery, a switch, a resistor, and an LED — a complete, working torch circuit.
What You Do
Breadboard it first, verify it lights, then confirm the resistor value against the LED’s rating.
What It Tells You
Even a one-LED circuit uses all four building blocks — power, input, processing, output.
The smallest project still teaches the full process

## Slide 16
MOD·05
CIRCUIT · BUILDING
Common Build Mistakes
Catch these before you ever apply power.
GOOD PRACTICE
1
Double-check polarity on every polarized part
2
Match resistor values to the schematic exactly
3
Build and verify one block before adding the next
COMMON MISTAKES
!
LED or electrolytic capacitor placed backwards
!
Wrong resistor value, read in a hurry
!
Whole circuit built and powered before any checks
Most build faults are visible before you ever apply power

## Slide 17
MOD·05
CIRCUIT · TESTING
Verify Before Power-On
The checks that catch a fault before it becomes smoke.
1
Check polarity
Every diode, LED, and electrolytic capacitor oriented correctly
2
Check for shorts
Continuity-test the rails before power ever touches the board
3
Check connections
Every wire seated firmly, no loose or half-inserted leads
4
Check power rating
Confirm the supply voltage matches what the circuit expects
A five-minute check beats a five-hour rebuild

## Slide 18
MOD·05
CIRCUIT · TESTING
Systematic Troubleshooting
Trace the signal instead of guessing at parts.
1
Confirm the power stage
Start at the source — no point testing further without power
2
Trace stage by stage
Follow the signal from input toward output, one block at a time
3
Compare to expected values
Use the schematic or a known-good build as your reference
4
Isolate before you replace
Confirm the exact faulty stage before swapping any part
Guessing replaces parts; tracing finds faults

## Slide 19
MOD·05
CIRCUIT · EXAMPLE
Real Example: The Continuity Tester That Didn’t Beep
A simple project, and a simple fault to match.
The Scenario
A hand-built continuity tester lights nothing and beeps at nothing, no matter what it touches.
What You Do
Trace from the battery outward, checking voltage at each stage until it stops appearing.
What It Tells You
Voltage stopped right after the switch — a single bad connection, not a bad design.
Tracing stage by stage finds the exact break

## Slide 20
MOD·05
CIRCUIT · DOCUMENTATION
Moving to Stripboard or PCB
From a temporary prototype to something that survives being carried around.
In Plain Terms
Once a breadboard circuit works, it moves to stripboard or a custom PCB for a permanent, solid build.
Real-World Picture
Like moving from a cardboard model to the finished, built structure.
Key Facts
Re-check every connection during the move — it’s a fresh build, not just a copy of the breadboard.
A working prototype still deserves a careful rebuild

## Slide 21
MOD·05
CIRCUIT · DOCUMENTATION
Documenting Your Build
Future-you will thank present-you for this.
1
Keep the schematic
The reference every future repair or change starts from
2
List your components (BOM)
Values, part numbers, and quantities in one place
3
Photograph the build
A picture catches wiring mistakes notes alone might miss
4
Record your test results
Voltages and behaviour when it was known to be working
Undocumented work is a repeat repair waiting to happen

## Slide 22
MOD·05
CIRCUIT · DOCUMENTATION
PCB Identification: Finding the Blocks on a Real Board
The four building blocks, hiding in plain sight.
1
Power section
Look for the input jack, large capacitors, and voltage regulator
2
Input section
Connectors, switches, or sensor headers near the board’s edge
3
Processing section
The largest IC on the board, usually near the centre
4
Output section
Connectors, LEDs, or driver transistors leading off the board
Every real board is just your four blocks, laid out physically

## Slide 23
MOD·05
CIRCUIT · PRACTICAL
Practical Exercise: Build an LED Flasher
Work through this list to build a simple 555-based flasher.
✓
Identify the four building blocks on the schematic
✓
Place power rails on the breadboard first
✓
Place the timer IC, resistors, capacitor, and LED
✓
Wire every connection, checking against the schematic
✓
Verify polarity and connections before applying power
✓
Power on and confirm the LED flashes as expected
If it doesn’t flash, trace before you rebuild

## Slide 24
MOD·05
CIRCUIT · REPAIR EXERCISE
Repair Exercise: Diagnose the Silent Circuit
A finished build that powers on but does absolutely nothing.
The Scenario
A completed project shows power is present, but the output never responds at all.
What Went Wrong
Signal was never traced stage by stage — a missed connection sat between input and processing.
How to Prevent It
Verify each block in sequence as you build, instead of wiring everything before testing anything.
Power present doesn’t mean the signal is getting through

## Slide 25
MOD·05
CIRCUIT · QUICK REFERENCE
Quick Reference: Common Schematic Symbols
A fast lookup for the symbols you’ll see most often.
SYMBOL
COMPONENT
LOOKS LIKE
KEY POINT
Zigzag / box
Resistor
A jagged line or rectangle
Limits current
Two parallel lines
Capacitor
Straight or curved plates
Stores charge
Triangle + bar
Diode
Arrow pointing to a line
Current flows one way
Three lines + circle
Transistor
Angled leads inside a circle
Switch or amplifier

## Slide 26
MOD·05
CIRCUIT · QUIZ
Quick Check
Talk through these before moving on to Module 6.
1
Question 1
Why does a schematic show connections instead of a physical picture of the parts?
2
Question 2
What are the four building blocks found in almost every circuit?
3
Question 3
Why test one section of a breadboard build before adding the next?
4
Question 4
Why trace a signal stage by stage instead of just swapping parts?
Discuss as a group before checking the answer key

## Slide 27
MOD·05
MODULE WRAP-UP
You Can Now…
By the end of this module, every recruit should be able to:
✓
Read a schematic and trace its signal flow
✓
Prototype a circuit correctly on a breadboard
✓
Identify the four building blocks in any circuit
✓
Verify a build before and after power-on
✓
Document a finished build so it can be repaired later
!
GOLDEN RULE
A schematic is a map — trace the path before you ever pick up a component.